## Slide 1: Arduino - Introduction
VSV Breda Airshow 2017
MakAIRsjop

## Slide 2: Introduction
Robert Haccou
  Electrical Engineer
  Engineer BPE Avionics
Royal Netherlands Air Force
  Main support-base, Woensdrecht Airbase
  MakAIRsjop
  Innovation centre AIR (Ambition - Innovation – Results)

## Slide 3: What is Arduino?
Development board
Programmable micro processor (Microcontroller)
(Digital) Electronics
Open source
Read inputs, control outputs!

## Slide 4: What can you do with Arduino?
Read inputs
  A finger on a button
  Light on a sensor
  Temperature in a room
  Data over communication bus
  Or a Twitter message
  More!
And turn it into an output
  Turning on a LED
  Activating a motor
  Text on a display
  Calculating / Processing
  Publishing something online
  More!

## Slide 5: Your first Arduino project!
Turn a LED ON and OFF (Output)
  Can become anything… Another time!
  More in’s and out’s… Another time!
With Arduino!

## Slide 6: But, how?
Wiring on the breadboard!
Programming the Arduino!
Testing!

## Slide 7: 1. Wiring the LED!
LED may be on any of the digital IO’s illustrated on the top of the Arduino)
Please note!: The LED must be wired with the long leg to the Arduino!

## Slide 8: 2. Programming
Start Arduino IDE
Make a new sketch
  Go to: File  New

## Slide 9: 2. Programming
Select the right board
  Go to: Tools  Board  Arduino/Genuino Uno
Select the right port
  Go to: Tools  Port  (Your com port)

## Slide 10: 2. Programming
Now we can start coding!
Make a variable ‘LED’ for your pin number!
int LED = 9;

## Slide 11: 2. Programming
Now we can start coding!
Initialize your pin as an INPUT or as an OUTPUT.
Use the function ‘pinMode’
pinMode(LED,OUTPUT);

## Slide 12: 2. Programming
Now we can start coding!
Use the function ‘digitalWrite’ to write a HIGH or LOW signal the LED go ON and OFF.
digitalWrite(LED, HIGH);
digitalWrite(LED, LOW);

## Slide 13: 2. Programming
Now we can start coding!
Use the function ‘delay’ to do nothing for a period of times in miliseconds
delay(1000); delays for 1second.

## Slide 14: 3. TESTING: Time to upload

## Slide 15: 3. TESTING
DOES IT WORK!?
IF (YES) Yay! You made your first Arduino Project!
IF (NO) No problem, let us help you!

## Slide 16: Questions?